## Slide 1: Engineering electrical stimulation of the human brain
David Caldwell
Thesis Defense - Bioengineering
Ojemann and Rao Laboratories
5.15.2019

## Slide 2: Thesis
Goal: To help engineer functional neuroprosthetics for sensory restoration and plasticity enhancement
Approach: Direct cortical stimulation (DCS) in humans through implanted electrodes can be engineered through:
  Models of its spread through cortex
  Interpretation of the underlying cortical dynamics during and in response to stimulation
  Impact on neuronal plasticity

## Slide 3: Outline
Introduction
  Clinical need
  Relevant physiology
  Direct cortical stimulation
Aims Overview
  Aim 1: Modeling cortical stimulation and interpreting its effects on neural dynamics
  Aim 2: Neural and behavioral effects of cortical stimulation in sensory cortex
  Aim 3: Engineered DCS protocols to induce changes in cortical connectivity, plasticity, and motor output mapping

## Slide 4: Motor deficits
Millions disabled from stroke
$34 billion - US/year
15-30% permanently disabled
Neuromodulation may be able to help over rehabilitation therapy alone
Stroke Facts | cdc.gov. 2016
Harvey RL, Winstein CJ. 2009
Lloyd-Jones D, et al. 2010

## Slide 5: Prior human stroke rehabilitation
BCI training and stimulation
  22 chronic stroke patients
  Activity timed peripheral nerve stimulation
  Effective neuroplastic induction
  Better rehabilitation outcome than BCI alone
Mrachacz-Kersting N, et al. 2015
EVEREST Clinical trial 2008
  Recovery of upper limb function following stroke
  Epidural stimulation during rehabilitation
  Discontinued - recent post hoc analysis suggests certain sub groups DID benefit
  Was “open loop”
Levy et al. 2016

## Slide 6: Motivated by activity dependent stimulation resulting in increased synaptic plasticity
Jackson A, Mavoori J, Fetz EE. 2006
Guggenmos, et al, 2013
Blackrock Neuro Med
Appropriate timing of stimulation
  Muscle activity
  Neural rhythm
Increase in connectivity strength1
Correlate with functional outcome?2

## Slide 7: Sensory deficits and restoration
Millions of individuals disabled due from paralysis
$40.5 billion US/year
For better neuroprosthetic performance, need sensory feedback
Chris Reeves Foundation
Bensmaia, SL, et al. 2014
Bensmaia, SL, et al. 2015

## Slide 8: Electrocorticography (ECoG)
Subdural implanted electrode array for epilepsy monitoring for one week prior to resection surgery
Record and stimulate
High quality signals from inside the skull
Direct measurements of electrical signals
1cm apart
2.3 mm radius
4.15 mm2 area

## Slide 9: Signals measured via ECoG
Lachaux J, et al, 2012
Slower oscillatory activity
  Theta (4-8 Hz), Alpha (8-12 Hz), Beta (12-30 Hz)
  Pulsed inhibitory activity, global communication
Broadband gamma activity (HG)
  Spectrum wide increase, masked in lower frequencies
  Focal neuronal activity

## Slide 10: Sensory processing, artificial feedback, and links to motor cortex
Ackerley R, et al, 2015
Bolognini N, et al, 2016
Natural Touch
Electric stimulation
Interplay between motor and sensory

## Slide 11: Neural effects of DCS
Borchers S, et al, 2012
Vincent M, et al, 2016
Complicated physiology
  Large axons stimulated first
  Axons preferentially over cell bodies
  Sometimes excitatory, sometimes inhibitory
Allows for direct interface with brain

## Slide 12: Aim 1.1: Creation of interpretable, analytic models that explain the resistivities of various cortical layers
Can we make a simple model that allows for rapid understanding of the current flow during electrical stimulation?
  Yes - Simple analytic model describes the data well (8 subjects thus far)
Range of literature values for cerebrospinal fluid, gray matter, white matter
  Important for source modeling, EEG, LFP propagation
  Forward finite element models (FEM) for patient specific stimulation
Contributes to field of targeted neuromodulation, and any modeling efforts using cortical layers
  Aim 1: Modeling cortical stimulation and interpreting its effects on neural dynamics

## Slide 13: Where do the currents go?
With Larry Sorensen, Jeneva Cronin, Stephen Reinertson, Brandon Yee, Dana Brooks, Moritz Dannhauer, Kimia Shayesterhfard, Rob MacLeod, and others
Bipolar, phasic electrical stimulation
Currents flow along electric field lines perpendicular to the equipotentials

## Slide 14: One layer apparent resistivity fits
Simple models fit well
  Extract “steady state” voltage
  Simple dipole model
Compare to collaborators Finite Element Models (FEM)

## Slide 15: Results across subjects and comparisons to the literature
Caldwell DJ, et al, “What is the resistivity of the human brain? Insights from direct electrical stimulation, electrocorticographic recordings of the human cortex, and analytic models”, BMC Neuroscience 2018, CNS 2018

## Slide 16: Characterizing ECoG electrodes
Charging double-layer capacitance
Capacitance + electrochemistry

## Slide 17: Multilayer analytic model analytic
Future work
  Include intraoperative DBS recordings
  Extend to recordings with depth electrodes to validate/predict
  Parameter space exploration on cluster to obtain range of physiological parameters

## Slide 18: Aim 1.2: Extraction of neural signals during concurrent DCS, and open source software and data to aid replication
How do we interpret the brain’s response to DCS?
  Continuous stimulation trains make interpretation difficult
Limited tools and data available for validating algorithm performance on stimulation related data sets
Provide code and data to advance artifact processing
6 example data sets already curated
Contributes to efforts across domains (hardware/software) to process neural data with stimulation (MEA + ICMS, EEG + TMS, ECoG)
  Aim 1: Modeling cortical stimulation and interpreting its effects on neural dynamics

## Slide 19: How we understand the cortical response to DCS?
Need to extract the ongoing neural activity to understand the neural response to stimulation
Stimulation artifact complicates traditional analysis
With Jeneva Cronin
Bingni Brunton
Nathan Kutz

## Slide 20: Sources of neural artifacts
Volume conduction through tissue
Linear addition if amplifiers don’t saturate
Residual artifact due to charge imbalance in tissue
Active area of research
  Hardware
  Software
Zhou A, et al, 2018
Notes: cut down on methods descriptions
show goals of project, results

## Slide 21: Problems with existing approaches
Linear interpolation eliminates high frequency information
Broadband gamma is an important signal (70-150 Hz)
Simple averaging blurs artifacts
Interpolated
raw

## Slide 22
Clustered dictionary based template matching technique
Detect onset/offset of each stimulation (z-score threshold crossing)
Dictionary of artifact templates, channel by channel (DBSCAN)
If there is a finite set, you can remove whichever one matches best
Wikipedia
Notes: talk about this less

## Slide 23: Can now examine time-frequency responses during time windows of stimulation
Stimulate here
Record everywhere else
Recover signals here

## Slide 24: Future work – validation and more advanced methods
Validation
  Lomb-Scargle periodogram1
  Synthetic data set2
New techniques
  Principal component regression2
  Dirichlet Process Mixture Model3
1. Muller L, et al, 2018
2. O’Shea DJ, et al, 2017
3. Teh YW, et al, 2006
4. http://austinrochford.com/posts/2016-02-25-density-estimation-dpm.html
Notes: belabor this a lot less
get rid of
put DBSCAN on this slide
What's more important
spend less time on details of others

## Slide 25: Aim 2.1: Slower response times to trains of DCS relative to natural haptic feedback in the same spatial location
How do humans respond behaviorally to DCS compared to natural, haptic feedback?
  Slower reaction times to DCS (4 subjects)
Contributes understanding of closed loop neuroprosthetic design criteria and sensory processing
  Aim 2: Neural and behavioral effects of cortical stimulation in sensory cortex

## Slide 26: Human cortical response times to natural haptic stimulation and DCS
Restoration of sensory feedback in a BCI application
How do humans respond to feedback through DCS?
Need to understand haptic (natural) compared to DCS (artificial) performance
Caldwell DJ, et al, “Cortical stimulation results in slower reaction times compared to peripheral touch in humans” in preparation: 2018
Jeneva Cronin
Kurt Weaver

## Slide 27: DCS of S1 results in slower response times (RT) relative to natural haptic touch
Different train lengths of DCS (100, 200, 400, 800 ms), all subjects demonstrate significantly slower reaction times to DCS relative to haptic touch, this matches the primate work of (Godlove J, et al, 2014)
Differences between these
Notes: This is the key takeaway from this graph *** apply this to
a few words to summarize key points
reduce text on slides
artifact processing

## Slide 28: No significant learning or habituation to blocked trials
Although DCS is novel, over a short period minimal learning effects
Suggests that DCS as administered here may always be responded to slower than haptic stimuli
Differences between these
Notes: Jeff says sensory response is pretty overlearned. Downward trend over time that eric is asking about?
raj says there is no feedback.
Bing says beep to motivate - getting better or worse. Clicker method
david bjanes - temporal dynamics are really slow.

## Slide 29: Aim 2.2: Comparisons between temporal dynamics and time-frequency responses to haptic stimuli and DCS in somatosensory cortex
What are the cortical differences between responses to natural haptic stimuli and DCS?
6 subjects (4 simple RT task, 2 waveform modification) collected, 2 to 4 additional subjects with varying waveforms would expand waveforms tested
Contributes to understanding of neural processing of artificial feedback, how to design future stimulation protocols to decrease latency
  Aim 2: Neural and behavioral effects of cortical stimulation in sensory cortex

## Slide 30: Continuing and future analyses time and frequency domain
Event related potentials (ERPs)
High gamma power (70-150 Hz)
Phase locking value (PLV)1
Phase amplitude coupling (PAC)2
1. Ai L, et al, 2014
2. Voytek B, et al, 2013

## Slide 31: Time series - haptic vs. DCS
Notes: compare those 2 pulses responses to the long train.
Stimulation parameters - how to get close to natural stimulation response
Dadarlat - something completely artificial, something learn. try and get stimulation as natural as possible. test if there is a particular combination of stimulation parameters. posthoc analysis, the more it is natural, does it approximate the natural response

## Slide 32
Time frequency - haptic vs. DCS
Notes: send Bing paper on lomb-scargle periodogram -
DCS - acronym - Chet said
DCES - direct cortical electriacl stimulation
DECS -
ECoS

## Slide 33: Modifications of the stimulation train inspired by onset/offset signals
What happens as we modify the shape of the waveform?
Can a stimulus train with greater charge initially more naturally activate somatosensory cortical circuitry?1,2
Tabot, GA, et al. 2013
Bensmaia, SJ, et al. 2015

## Slide 34: Similar perceptual reports, trend towards faster reaction times
Trend towards faster RT with initial high pulses
  (median of 414 vs 473 ms)
No statistically significant difference between groups
Similar perceptual reports

## Slide 35: Different size of evoked responses

## Slide 36: Increased charge delivery decreases RT
All DCS trains are 200 ms trains
2 individual pulses can be perceived
800 μA train not perceived
Notes: stimulate with higher frequencies, inhibitiory effect might contribute. Higher than 100 Hz, hyperpolarizing neurons.
Chet said they can tell difference between 50-100 Hz
David bjanes different breaks between trains. O'doherty 200 -400 hz, put breaks of start in stop in trains, cueing off of break
David bjanes - talk to him again
Raj - get animal data -
2011/2013 - azadeh - compare predictions to animal data

## Slide 37: Aim 2.3: The behavioral and neural effects of temporally simultaneous and spatially overlapping haptic stimuli and DCS
What happens behaviorally and neurally when natural and artificial feedback are combined spatially and temporally?
Can they be perceived independently?
Does the difference in response times predict where there will be uncertainty in their timing?
2 subjects collected, 2 to 4 more with one protocol would provide more significance and brain area covered
Contributes to understanding of real world neuroprosthetics where different stimuli modalities will arrive concurrently
  Aim 2: Neural and behavioral effects of cortical stimulation in sensory cortex

## Slide 38: Temporal order judgement task

## Slide 39: Temporal order judgement results
DCS must lead natural touch by approximately the lag between them to be perceived as arriving first
Stimulus onset asynchrony (SOA), 50% point on gaussian

## Slide 40: Functional MRI correlates of TOJ
Takashi T, et al, 2013
Miyazaki M, et al, 2016
fMRI reveals areas of interest
  left ventral, bilateral dorsal premotor cortex
  left posterior parietal
  bilateral premotor cortices
  bilateral middle frontal gyri
  bilateral inferior parietal cortices and supramarginal gyri
  bilateral posterior part of the superior and middle temporal gyri
Analyze neural signals focused on these regions

## Slide 41: Aim 3.1: Beta-oscillation triggered stimulation paradigm to enhance connectivity of beta-synchronous regions
Based off of prior work with beta-oscillation driven stimulation, can we observe similar effects of stimulation in humans?
  Data collected from 7 subjects
  Dose dependent enhancement,
  Exploration of dependence on phase, connectivity patterns
Contributes to understanding of protocols to engineer plasticity from model systems
Aim 3: Engineered DCS protocols to induce changes in cortical connectivity, plasticity, and motor output mapping

## Slide 42: Beta stimulation experimental paradigm
Jeremiah Wander
Jared Olson
Caldwell DJ, et al, “Cortical stimulation results in slower reaction times compared to peripheral touch in humans” in preparation: 2018

## Slide 43: Measurement of EP
Size of evoked potential 10-30 ms after stimulation, early excitatory component1
Measure peak, quantify change relative to baseline
1. Entz L, et al, 2014

## Slide 44: Randomized Control Stimulation
Playback effect
No statistical significance (ANOVA, Multiple comparisons), within playback
Other than baseline, every beta-triggered statistically different than playback (ANOVA, multiple comparisons).

## Slide 45: Real time filtering
Real time filtering (12-20 Hz) + artifact blanking
Real time test of digital filtering
  Non linear phase IIR filter

## Slide 46: Accuracy of phase delivery (unimodal)
Phase delivery
Non-linear curve fit with sine wave 50 – 0 ms before stimulation
Bootstrap distribution to get an idea of reliability of phase estimate

## Slide 47: Accuracy of phase delivery (broad, multiple peaks)

## Slide 48: Effect across subjects
Current conclusions
  Dose dependent effect
  Phase is not biggest factor, but may matter
Future work
  Characterize changes in resting state connectivity (enhancement in beta, decrease in other frequencies)
  Correlate accuracy of phase delivery with magnitude of effect

## Slide 49: Aim 3.2: Paired pulse stimulation to enhance connectivity between two cortical sites
Can a paired pulse paradigm enhance connectivity between two cortical sites in humans and demonstrate an increase in functional output (muscle activity)?
1 subject collected, 4 more for validation of single parameter, 8 for different parameters
Contributes to understanding of simple plasticity protocols (no activity dependence), and potential to use MEP output to correlate with plasticity in humans
Aim 3: Engineered DCS protocols to induce changes in cortical connectivity, plasticity, and motor output mapping

## Slide 50: Paired pulse conditioning in DBS patients
Intraoperative DBS placement
ECoG strip placed temporarily
Can perform somatosensory evoked potentials (SSEPs)
  Locate central sulcus
Motor evoked potentials (MEPs)
  Assess cortical excitability / changes in plasticity

## Slide 51: Paired pulse conditioning and connectivity assessment - facilitation

## Slide 52: Paired pulse conditioning and connectivity assessment - depression
Seeman S, et al, 2017

## Slide 53: Aim 3.3: EMG triggered stimulation to remap motor cortex output
Aim 3: Engineered DCS protocols to induce changes in cortical connectivity, plasticity, and motor output mapping
Can EMG triggered stimulation enhance connectivity between two sites in motor cortex and change motor output patterns?
With 2 subjects, validation of protocol, 5 subjects, more comprehensive results on generalizability
Contributes to understanding of different activity dependent signals for plasticity induction

## Slide 54: EMG triggered stimulation changes motor output
Lucas T, Fetz E, 2013

## Slide 55: EMG triggered stimulation in humans
Trigger off EMG amplitude over threshold (site A, biceps region) in electrodes for different region (site B, deltoid)
Stimulate MEPs at site A, observe muscle response similar to site B
  (dynamic time warping, hierarchical clustering1 on EMG)
Measure EPs at site A, site B
1. Aghabozorgi S, et al, 2015

## Slide 56: Thesis Contributions
Aim 1:
  Complementary approaches to complicated FEM models
  Better understanding of resistivities of cortical layers for modeling
  Additional methods, data sets for processing stimulation related data
Aim 2:
  Understanding of behavioral and neural processing of DCS
  Comparisons to natural feedback within same subject
  Different engineered DCS protocols and their effects
  Understanding of real world scenario of concurrent feedback
Aim 3:
  Testing of various stimulation protocols previously demonstrated in model systems
  Moves protocols towards clinical trials

## Slide 57: Timeline
June - July 2018 : Write paper on analytic model for stimulation voltage currents
  Sufficient data has been collected
August 2018 : Submit oscillation triggered plasticity paper
  Sufficient data has been collected
June - February 2019 :
  ECoG patient data collection
    waveform modification subject – 2 to 4 subjects
    temporal order judgement task - 2 to 4 subjects
    EMG triggered stimulation -2 pilot subjects validate protocol, 5 subjects generalize
  DBS subject data collection
    4 to 8 pair pulse stimulation subjects to assess viability of MEPs, extent of parameters tested
January 2019: Establish reading committee
January-February 2019: Write paper on differences between natural and cortical feedback
January-February 2019: Write paper on temporal order judgement and subjective judgement
March - May 2019: Write dissertation
Beginning of May 2019 (3 weeks prior to exam): Dissertation sent to all committee
members
May 30 2019: Dissertation Defense

## Slide 58: Thank you! Acknowledgments
University of Washington
Jeffrey Ojemann
Rajesh Rao
Bingni Brunton
Nathan Kutz
Larry Sorensen
Jeneva Cronin
Kurt Weaver
Nile Wilson
Clark Kuo
Jared Olson
Andrew Ko
Jeremiah Wander
Nancy Wang
James Wu
Kaitlyn Casimo
Brandon Yee
Gabriel Obregon Devapratim Sarma
Brady Houston
Northeastern
Dana Brooks
Kimia Shayestehfard
University of Utah
Rob MacLeod
Moritz Dannhauer
University of Freiburg
Tonio Ball
Alexis Gkogkidis
Notes: Contributions slide - what would my major contributions
what are collateral contributions - results to DBS, ECoG
Individual aims - break down what already has done, break timeline down for each aim, at different

## Slide 59: Supplemental slides

## Slide 60: Origins of high gamma
Miller KJ, et al, 2009

## Slide 61: Optical imaging of DCS
Borchers S, et al, 2012

## Slide 62: Aim 1.1: Creation of interpretable, analytic models that explain the resistivities of various cortical layers

## Slide 63: Two separated electrodes

## Slide 64: Multilayer equations
Schumann G, et al, 1969
Constant voltage finite size circular electrode – V(r) is voltage on the surface away from the electrode

## Slide 65: Comparison to FEM

## Slide 66: Aim 1.2: Extraction of neural signals during concurrent DCS, and open source software and data to aid replication

## Slide 67: Dirichlet process mixture model
El-Arini K, 2008

## Slide 68: Dirichlet process mixture model
http://austinrochford.com/posts/2016-02-25-density-estimation-dpm.html

## Slide 69: (3) Artifact isolation
Motivation:
  Stimulation artifact 1000x greater than evoked potentials
  Cannot filter or perform traditional time-frequency analyses

## Slide 70: ICA components on a trial by trial basis
Isolate components
Certain peak prominence
Occur within stimulation window
Currently requires tuning, scaling

## Slide 71: Example of original signal vs. extracted signal
Artifact largely eliminated
Signal underneath appears preserved
Not perfect removal

## Slide 72: Wavelet analysis example
Trial by trial time frequency analyses
Notch filtering

## Slide 73: Procrustes distance metric trial by trial
Trial by trial analysis (10 trials here)
Stimulation channels excluded
Channel variability
Future work to determine cutoff, applicability across data sets
Stimulation
electrodes
Worse
Better

## Slide 74: Aim 2.1: Slower response times to trains of DCS relative to natural haptic feedback in the same spatial location

## Slide 75: Characterizing the touch probes
Notes: Contact Henrik ehrsson – email Arvid
Pneumatic would be better
Fill out this curve!!!!!

## Slide 76: Aim 2.2: Comparisons between temporal dynamics and time-frequency responses to haptic stimuli and DCS in somatosensory cortex

## Slide 77: Aim 2.3: The behavioral and neural effects of temporally simultaneous and spatially overlapping haptic stimuli and DCS

## Slide 78
From: Neural Correlates of Tactile Temporal-Order Judgment in Humans: an fMRI Study
Cereb Cortex. 2012;23(8):1952-1964. doi:10.1093/cercor/bhs179
Cereb Cortex | © The Author 2012. Published by Oxford University Press. All rights reserved. For Permissions, please e-mail: journals.permissions@oup.com
Notes: Figure 5. Brain areas activated by TOJ (red), random-dot motion (blue), and a listening task (green). (A) Lateral views. (B and C) Activations on 2 transverse planes at z = + 6 mm (B) and +42 mm (C). Activation maps are shown in red for the TOJ > NJ contrast (the same conjunction analysis as in Fig. 4), in blue for the motion > no motion contrast during the task involving moving random dots, and in green for the forward replay > reverse replay contrast during the narrative listening task. All contrasts were thresholded at P = 0.05 (uncorrected). White represents commonly activated area in TOJ > NJ overlapped with the area activated by the moving random dots. Note the overlap in the posterior regions of the bilateral middle temporal gyri (B), and in the bilateral dorsal premotor cortices and in the bilateral inferior parietal cortices (C). The x signs in (B) represent the standard locations of the human V5/MT (a: [−46, −66, 8] (Dukelow et al. 2001), b: [−46, −78, 6] (Kolster et al. 2010), c: [−55, −74, 4] (Orban et al. 2003), and d: [−46, −73, 3] (Watson et al. 1993) in the MNI coordinates). The yellow dots in (B) represent reported peak activations in response to biological motion stimuli (1: [−55, −21, 7], [61, −24, 6] (lip-reading, Calvert et al. 1997), 2: [−46, −71, 8], [47, −59, 9] (gaze, Wicker et al. 1998), 3: [−48, −55, 7], [54, −50, 3] (gaze, Puce et al. 1998), 4: [−50, −52, 4], [55, −50, 3] (mouth movement, Puce et al. 1998), 5: [−47, −57, 14], [55, −65, 5] (gaze, Hoffman and Haxby 2000), and 6: [51, −36, 5] (hand movement, Grezes et al. 1999). The x signs in (C) represent the same locations in the human VIP as in Figure 4.
78

## Slide 80: Aim 3.1: Beta-oscillation triggered stimulation paradigm to enhance connectivity of beta-synchronous regions

## Slide 81: Rhythms in the brain
Idea of “Beta-Rhythms”
  12-25 Hertz
  Representative of synchronous neural activity across the cortex
  Neural Correlate of attention
  Transient synchronization
http://itsusync.com/different-types-of-brain-waves-delta-theta-alpha-beta-gamma
Murthy VN, Fetz EE. 1996a, 1996b

## Slide 82: Non-human primate work from Fetz lab
Stimulation during depolarizing phase – strengthen synaptic strength
Stimulation during hyperpolarizing phase – weaken synaptic strength
Zanos S.. 2013.
0.5 mm exposed tip (0.06mm2 area) epidural electrodes

## Slide 83: How do we measure short term plasticity changes?
Keller CJ, et al, 2014
Cortico-cortical evoked potentials (CCEP)
Early component (10-50 ms post stimulation) - excitatory
Late component (100-300 ms post stimulation) – inhibitory
Measure modification of these

## Slide 84: (1) Beta stimulation project
Motivation: Enhance connections in the brain for neurorehabilation
Goal: Test a spontaneous beta-oscillation driven closed loop stimulation protocol to modify short term plasticity in humans

## Slide 85: Beta stimulation experimental paradigm
Olson JD*, Caldwell DJ*, et al. “Dose dependent enhancement of Cortico-Cortical Evoked Potentials during Beta-Oscillation Triggered Direct Electrical Stimulation of Human Cortex”,
In Preparation
*These authors contributed equally

## Slide 86: Calculating phase of delivery
Method:
  Levenberg–Marquardt algorithm
  Fit sine wave (10-30 Hz) from 50 ms before to the time of stimulus on the raw and causal beta filtered signal
  Estimate instantaneous delivery phase
  Some subjects within 4° of phase delivery on average – others 100 °

## Slide 87: Spatial selectivity – no clear phase dependence
Channels adjacent to stimulation sites
  Do not always show evoked potentials
  Effective connectivity
Example of no clear phase dependence
  Both 90, 270° show effect

## Slide 88: CCEP magnitude trend depending on number of conditioning stimuli
Dose dependent effect
Across subjects
Phase not as important as in primate studies
  Different electrode sizes, lengths of experiments, numbers of sessions
11% increase in CCEP magnitude

## Slide 89: ANOVA results across subjects and phase
Variability:
Size of response
Degree of response
Why?
Electrode placement
Subject differences
Ongoing brain state
Medication status

## Slide 90: Playback condition – does beta matter?
Playback effect
  No statistical significance (ANOVA, Multiple comparisons), within playback
Other than baseline, every beta-triggered statistically different than playback (ANOVA, multiple comparisons).
Significant difference between subjects
Why higher baseline?

## Slide 91: (1) Beta triggered stimulation summary
7 subjects
Transient increase in CCEP magnitude
Individual subject variability
No clear phase dependence
Smaller effect without beta oscillation

## Slide 92: Aim 3.2: Paired pulse stimulation to enhance connectivity between two cortical sites

## Slide 93: Pre vs . post

## Slide 95: Aim 3.3: EMG triggered stimulation to remap motor cortex output

## Slide 96: Other work

## Slide 97: Neural data exists in a high-dimensional space
Represent connectivity data as data matrix
Across frequencies, between channels
Can be directional, complex valued

## Slide 99: Beta Stimulation Brain Compilation

## Slide 100: Physiology of Cortico-Cortical Evoked Potentials
Keller CJ, Honey CJ, Mégevand P, Entz L, Ulbert I, Mehta AD. Mapping human brain networks with cortico-cortical evoked potentials. Philos Trans R Soc Lond B Biol Sci. 2014;369(1653). doi:10.1098/rstb.2013.0528.